BLN Esante Windows Vista Support Program – Ver. 1.03

Install Procedure

** CAUTION!! **

If you connect your machine to a PC with Windows VISTA, it will not work properly.

Please install this program and upgrade your machine, even if you are not a Windows Vista owner.

To use your machine connected to a PC with Windows VISTA, please read the following.

Two cases below are possible:

CASE A:  You have Windows VISTA only

(  Please contact a dealer shop located near you.

CASE B:  You have access to another OS (Windows®98SE/Me/2000/XP Home/Professional)

other than Windows VISTA.

(   Please be sure to install the program to your machine by a PC with

Windows®98SE/Me/2000/XP Home/Professional, following the “Program Install

Procedure” as outlined on following page.

Do not use Windows VISTA for this installation.

Once you install the program, you can upgrade your machine directly using Windows

VISTA for the next version.

>> How to confirm whether your machine supports Windows VISTA or not

Program Install Procedure

**NOTE**

- Before you update your machine to Ver.1.03, please be sure to install this Windows VISTA support program first. Your machine could be damaged otherwise.

- Please install this program and upgrade your machine, even if you are not a Windows Vista owner.

| 1. | Press and hold the "Presser Foot Lifter" button while turning on the machine. The following screen appears. |
| --- | --- |
|  | If "VER 2" appears in the lower right portion of the screen as pictured below, the sewing machine already supports Windows Vista®. You do not need to follow the steps below for supporting it. Please follow "To confirm the software version of your sewing machine" and upgrade your software to the latest version. |
| 2. | Create a temporary folder (ex. C:\Temp) on your PC to save the support program file to be downloaded. |
| 3. | Click the "Download d6mvista.upg(Support program)" |
| 4. | Select the previously created temporary folder (ex. C:\Temp) where the downloaded file should be stored. Download the file. |
| 5. | Plug the USB cable connectors into the corresponding USB port connectors for the computer and for the machine. The "Removable Disk" icon appears in "My Computer" on the computer. |
| 6. | Copy the "d6mvista.upg" file to "Removable Disk". The message "Connected to PC. Do not disconnect the USB cable." appears. |
| 7. | When the screen shown in step 1 appears again, press "LOAD". The message "Saving the upgrade file. Do not turn main power to OFF." appears. |
| 8. | When the following screen appears, turn the machine off and then on again. |
| 9. | When the following screen appears, press "LOAD". |
| 10. | The message "Saving the upgrade file. Do not turn main power to OFF." appears. **CAUTION** Never turn off the machine while this message is shown. The machine could be damaged. |
| 11. | The machine will re-start automatically after about 10 seconds and then the following screen will appear. Confirm that "VER 2" appears in the lower right portion of the screen. |
| 12. | Create a temporary folder (ex. C:\Temp) on your PC to save the update program files to be downloaded. |
| 13. | Click the "Download d6mbu1031.upg(Software-1/2)" link below. Download d6mbu1031.upg(Software-1/2) |
| 14. | Select the previously created temporary folder (ex. C:\Temp) where the downloaded file should be stored. Download the file. |
| 15. 16. | Then click the "Download d6mbu1032.upg(Software-2/2)" link below. Download d6mbu1032.upg(Software-2/2) Repeat step 14 above. You can upgrade your machine by the following method. Please refer to link below: Instruction PDF (PDF file, 72KB) ** NOTE ** For convenience of the upgrade process, the file called "PROUPCK2.D6Q" is created in the "Removable Disk", but there is no harm if you leave it. Even though this file exists, you can upgrade your software to the latest version normally. |

To confirm the software version of your sewing machine

| 1. | Press the main power switch to turn on your machine and then touch the screen. |
| --- | --- |
| 2. | Press the Setting Mode Key in the upper left corner of the display. |
| 3. | Go toward p.5, and you can see the software version number. (If the version is already v.1.03 or higher, it is not necessary to update your machine with the program on this page.) |

How to update your machine's software

| 1. | Create a temporary folder (ex. C:\Temp) on your PC to save the update program files to be downloaded. |
| --- | --- |
| 2. | Click the "Download d6mbu1031.upg(Software-1/2)" link above. |
| 3. | Select the previously created temporary folder (ex. C:\Temp) where the downloaded file should be stored. Download the file. |
| 4. 5. | Then click the "Download d6mbu1032.upg(Software-2/2)" link above. Repeat step 3 above. |
|  | You can upgrade your machine by the following method. Please refer to link below. Instruction PDF (PDF file, 72KB) |

--- UPDATE HISTORY DETAIL ---

Version 1.03 (May, 2008)

Version 1.03 update provides the following changes:

- The data of Satin Stitch Pattern, "8-07" was changed.

Version 1.02 (January, 2007)

- Support for Windows Vista® - your machine is now supported by the Windows Vista® operating system.

Version 1.01 (September, 2005)

Version 1.01 update provides the following changes when embroidery or embroidery edit is

selected:

- Reduction of noise when feeding the fabric.

- Spelling of the thread color name LEMONY YELLOW will corrected to LEMON YELLOW.

- Reading of the mirror image and multi-color editing changes made in other models will transfer to your machine correctly. So will Writing from your machine to other models.